Tim Duffy
CS 455 - PA 2
Error Control Protocols
Design
This program simulates a network capable of sending information in one direction (from A to B). There are protocols in place to ensure that the data transferred arrives to the receiver in the correct order, and that the data has not been altered by bit errors over the course of transmission.
The way this program functions is fairly simple. Messages are sent from the application layer (layer 5) on the A side. They are then transmitted using a Go-Back-N protocol to the receiver (B). Go-Back-N allows A to send N packets of information to B at a time (meaning up to N packets can be in the network at once). Finally, packets are sent to the B-side application layer in order. Let us examine the protocols that make this possible:

- In Order Arrival: To ensure in order arrival, the receiver only accepts packets with the sequence number it is expecting. If B receives a packet it has already seen (duplicate packet suggests that the ACK previously sent for this packet was lost) is it ignored. Likewise, if a packet arrives out of order, it is ignored as well.
Sequence numbers are set up so that no 2 packets with identical sequence numbers can be in the network at once. This way we can utilize cumulative ACKs. That is, an ACK for sequence number N tells A that packet N and every packet before N have been received successfully.

- Secure delivery (bit error detection): To find bit errors in packets, which often occurs in networks, we use a checksum. This is an number which holds the sum of each number in the header (sequence number, ACK number) and each letter in the payload. Upon arrival of a packet (to both A and B sides) the checksum is checked. If the packet has experienced a bit error, the checksum will not match the sum of the header and payload data. If the checksum is correct, then the packet is not corrupt. Any packet found to be corrupt is ignored.

- Packet loss: To determine packet loss in the network, we use a timer on the A side. Once a packet is sent to B, the timer is started. If an ACK for that packet is not received within the specified timeout interval, it is assumed that the packet was lost on its way to B. If the packet was lost, B will reject all other arriving packets. Therefore, when a timeout event occurs, the entire window is resent.
There are a few things that could be done to improve the performance of this program. One option is that we can store any out of order packets that arrive at B. We can do this by storing any out of order packets that we have not seen already (we would still ignore duplicate packets). Instead of cumulative ACKs, we would send ACKs for packets we received, and NACKs for any packet we are missing. A would then only retransmit packets that it received a NACK for.
Another thing that could be done is to use a retransmit interval that changes during the simulation. Each time a new ACK is received, we can calculate RTT. If we calculate average RTT each time a new ACK comes in, incorporating this new value each time, we could estimate RTT pretty well. We could then set the interval to a multiple of this estimated RTT, instead of having one static value.

Testing
Steps needed to run this program are very straightforward. After compiling all of the source code files, run Project.java. This file contains the main function for the program, and is responsible for creating the network simulator. Once the program begins, follow the prompts on the screen, and enter the correct values. The values you must enter are:
1) Number of messages to simulate: This is the number of messages that will be sent	down from Layer 5 (on sending side). Note that the simulation terminates after the	last message is sent from layer 5. This means that it is likely for some messages	to be sent down from A, but not yet received by B when the simulation ends.

2) Packet loss probability: Average percent of packets to be lost in the network
3) Packet corruption probability: Average percent of packets (that have not been lost	to be lost in the network) to arrive corrupted. This simulates bit errors that	often occur over a link.
4) Average time between messages from sender's layer 5: The smaller the number, the	faster packets will arrive, and the faster the sending window/queue will fill up.
5) Window size: How many packets may be in the network before receiving an ACK.
6) Retransmission timeout: How long a timer will run before expiring. If an ACK has	not been received when the timer expires, the entire window will be resent to B
7) Trace level: For debugging purposes. 0 will display no messages regarding network	events (except the print statements I included in the program), while 3 will	display significantly detailed information.
8) Seed number: Used for random number generators.

To ensure that my protocols were working correctly, I ran the simulation several times, on different seed numbers. Each test run sent a high volume of messages (1000 messages to be exact), used a window size of 1, and a timeout interval of 20. The protocols work correctly since, even with significant probability of loss and corruption (0.2 for each), packets were delivered in order. All test runs have shown that all packets arrive in order, which suggests that all protocols are functioning correctly.

Data
Here, I analyze to relationship between probability of packet loss and RTT, and probability of packet corruption and RTT. Each set of packet loss/corruption uses 5 independent test runs, which are then averaged together.

To ensure that packet loss/corruption is the only factor playing a role in RTT, we will use the following standards for all of our trial runs:
 - 1000 messages sent from Layer 5
- Average interval from senders Layer 5: 10
- A window size of 8
- A RxmtInterval of 20.0

Seeds chosen at Random
Seed for Run 1: 7262
Seed for Run 2: 3815
Seed for Run 3: 6253
Seed for Run 4: 1180
Seed for Run 5: 4507
Tests for packet loss:
0.0 Loss, 0.0 corruption
	Run 1 / (7262)	Run 2 / (3851)	Run 3 / (6253)	Run 4 / (1180)	Run 5 / (4507)
Total Packets	1000	1000	1000	1000	1000
# Original	1000	1000	1000	1000	1000
# ACKs	1000	999	1000	1000	1000
# Rxmts	0	0	0	0	0
# Lost	0	0	0	0	0
% Lost	0	0	0	0	0
# Corrupt	0	0	0	0	0
% Corrupt	0	0	0	0	0
Avg RTT	37.9977 ms	32.0697 ms	34.627 ms	37.9924 ms	33.2169 ms

Average RTT of 5 Runs: 35.18074 ms

0.25 loss, 0.0 corruption
	Run 1 / (7262)	Run 2 / (3851)	Run 3 / (6253)	Run 4 / (1180)	Run 5 / (4507)
Total Packets	3657	3357	3593	3383	3695
# Original	87	205	111	186	135
# ACKs	79	197	103	178	127
# Rxmts	3570	3152	3484	3197	3560
# Lost	918	916	920	840	941
% Lost	0.25	0.27	0.26	0.25	0.25
# Corrupt	0	0	0	0	0
% Corrupt	0	0	0	0	0
Avg RTT	2547.6481 ms	2145.4434 ms	2242.464 ms	1873.579 ms	1874.9479 ms

Average RTT of 5 Runs: 2136.81648 ms

0.5 loss, 0.0 corruption
	Run 1 / (7262)	Run 2 / (3851)	Run 3 / (6253)	Run 4 / (1180)	Run 5 / (4507)
Total Packets	3176	3171	3745	3717	3194
# Original	388	382	78	87	378
# ACKs	380	377	78	87	374
# Rxmts	2788	2789	3667	3630	2816
# Lost	1753	1771	1872	1884	1786
% Lost	0.55	0.56	0.5	0.51	0.56
# Corrupt	0	0	0	0	0
% Corrupt	0	0	0	0	0
Avg RTT	4676.3717 ms	4986.3324 ms	681.2206 ms	732.3429 ms	4568.7535 ms

Average RTT of 5 Runs: 3129.00422 ms

0.75 loss, 0.0 corruption
	Run 1 / (7262)	Run 2 / (3851)	Run 3 / (6253)	Run 4 / (1180)	Run 5 / (4507)
Total Packets	3849	3776	3819	3866	3864
# Original	22	74	61	11	116
# ACKs	22	74	61	11	116
# Rxmts	3827	3702	3758	3855	3748
# Lost	2845	2874	2869	2909	2990
% Lost	0.74	0.76	0.75	0.75	0.78
# Corrupt	0	0	0	0	0
% Corrupt	0	0	0	0	0
Avg RTT	518.7039 ms	2515.2561 ms	1488.4866 ms	106.021 ms	3416.6742 ms

Average RTT of 5 Runs: 1609.02836 ms

Tests for packet corruption:

0.25 corruption, 0.0 loss
	Run 1 / (7262)	Run 2 / (3851)	Run 3 / (6253)	Run 4 / (1180)	Run 5 / (4507)
Total Packets	3752	3782	3748	3725	379
# Original	60	65	63	59	65
# ACKs	52	57	55	51	57
# Rxmts	2692	3717	3685	2666	3734
# Lost	0	0	0	0	0
% Lost	0	0	0	0	0
# Corrupt	970	925	938	968	984
% Corrupt	0.26	0.24	0.25	0.26	0.26
Avg RTT	2120.6493 ms	2477.3256 ms	2157.5543 ms	1756.2987 ms	1862.8415 ms

Average RTT of 5 Runs: 2074.93388 ms

0.5 corruption, 0.0 loss
	Run 1 / (7262)	Run 2 / (3851)	Run 3 / (6253)	Run 4 / (1180)	Run 5 / (4507)
Total Packets	3850	3808	3951	3740	3914
# Original	39	43	41	54	38
# ACKs	32	35	34	50	32
# Rxmts	3811	3765	3910	3686	3876
# Lost	0	0	0	0	0
% Lost	0	0	0	0	0
# Corrupt	1939	1836	2022	1912	1998
% Corrupt	0.5	0.48	0.51	0.51	0.51
Avg RTT	2273.7896 ms	3389.4766 ms	3035.4832 ms	1881.1553 ms	2156.9614 ms

Average RTT of 5 Runs: 2547.37322 ms

0.75 corruption, 0.0 loss
	Run 1 / (7262)	Run 2 / (3851)	Run 3 / (6253)	Run 4 / (1180)	Run 5 / (4507)
Total Packets	3865	3880	3855	3838	3951
# Original	15	9	27	27	25
# ACKs	15	9	19	27	19
# Rxmts	3850	3871	3828	3811	3925
# Lost	0	0	0	0	0
% Lost	0	0	0	0	0
# Corrupt	2913	2879	2909	2891	2984
% Corrupt	0.75	0.74	0.75	0.75	0.76
Avg RTT	1638.0761 ms	109.2398 ms	3512.396 ms	1455.6364 ms	2650.5748 ms

Average RTT of 5 Runs: 1873.18462 ms